## Slide 1
Cost of Quality (COQ)
Problem
How to minimize the cost of quality?
Define quality goals; COQ of 10–15% may be OK
Collect cost data: internal failure, external failure, appraisal, prevention
Identify which quality costs should be reduced (if any), then use appropriate methods for each:
  For Internal Failure costs: Poka-Yoke (Mistake-Proofing), Root Cause Analysis,…
  For External Failure costs: Customer Surveys, Warranty Programs, …
  For Appraisal costs: Statistical Process Control (SPC), Statistical inspections, …
  For Prevention costs: Audits, Employee Training, …
Implement determined quality improvements.
Repeat
Minimize
Cost of Quality
Find 4 costs making up cost of quality
Choose which cost to reduce
Implement quality improvements
Copyright © 2024 Dan Zwillinger. All rights reserved.
Cost of Quality=COPQ+COGQ
Cost of Poor Quality (COPQ)
  cost associated with poor-quality products/services
  = Internal Failure costs + . External Failure costs
Cost of Good Quality (COGQ)
  cost to prevent poor-quality products/services
  = Appraisal costs + . Preventative costs
Difficulty
Work with an SME
Quality level
Quality cost per unit
COGQ
COPQ

## Slide 2
Cost of Quality (COQ) – Example – Making widgets
Copyright © 2024 Dan Zwillinger. All rights reserved.
Imagine we are making widgets.
The per unit costs of good quality (COGQ) and poor quality (COPQ) are below
For COGQ: it is very expensive to have a low failure rate
  For example: recalibrate machines every hour, update employee training weekly, many inspections of incoming materials, …
For COPQ: it is very expensive to have a high failure rate
  For example: recalls, replacements, customer ill-will, …
Hence, there is a value where the total cost of quality (COQ) is least.
  In the example, the COQ is minimized at $22/unit at a common failure rate of 15%
failure rate
cost
COGQ
COPQ
COQ
failure rate

## Slide 3
Cost of Quality (COQ)
Slide 1
Slide 2
There is a cost just to determine the COQ.
In the example, the failure rates of COGQ and COPQ are the same, this will not be true in general.
Copyright © 2024 Dan Zwillinger. All rights reserved.
Recommended web sites for more information
https://www.whatissixsigma.net/cost-of-poor-quality/
https://www.compliancequest.com/cq-guide/copq-categories-prevention/
COQ applies beyond manufacturing to nearly any product or service (e.g., code reviews for software or exit interviews for personnel management).
The 1-10-100 rule states that that one dollar spent on prevention will save 10 dollars on correction and 100 dollars on failure costs.
Preventive costs include: holding contract reviews, performing market research, assessing process capability, performing quality audits, performing supplier evaluations, training.
Appraisal costs include: ensuring calibration, holding inspections at multiple points in the value stream, training.
Internal failure costs include: performing failure analyses, scrap, testing, repair, rework
External failure costs include: customer engagements, investigations, loss of goodwill, financial penalties, cost to replace or repair.